## Slide 1: FOTA on top of MMDV-3.1.0
Christophe GUIBOUT

## Slide 2: FOTA overview
FOTA backend server
STM32MP1x
download
FOTA server
New STM32MPx image to be deployed
Update manager
Partitions A
Partitions B
flash
flash
Check for update
Boot selection

## Slide 3: MMDV-3.1.0 Layout
External Storage
TF-A (BL2) (Copy 2)
BOOTFS
ROOTFS
VENDORFS
USERFS
#4
#5
#6
#7
#3
TF-A (BL2) (Copy 1)
#2
#1
FIP
TF-A
TF-A STM32 Header
BL2 DT
BL2
FIP
TEE PAGEABLE
HW-CONFIG (DT)
UBOOT
TEE HEADER
TEE CORE + DT
BOOTFS (ext4)
uImage
Device tree
cmdline
ROOTFS (ext4)
Linux root filesystem
VENDORFS (ext4)
3rd part proprietary binaries
USERFS (ext4)
User data
examples
Notes: FIP partition contains TF-A BL32 or OPTEE and u-boot
  Secure services have some dependencies with kernel and need to be updated together
TF-A BL2 is in charge of DDR init and FIP partition load
  BL2 doesn’t contain feature that needs to be updated
  FOTA mechanims will be managed inside BL2

## Slide 4: FOTA Layout A/B mechanism
External Storage
TF-A (BL2) (Copy 2)
BOOTFS
ROOTFS
VENDORFS
USERFS
FIP
#4
#8
#5
#6
#7
#3
TF-A (BL2) (Copy 1)
#2
#1
FIP
BOOTFS
ROOTFS
VENDORFS
#11
#10
#9
Partition A
Not updated partition
Partition B
BL2 is not safely updatable. It manages OTA by reading metadata.
Updatable partitions are duplicated (A/B mechanism)
userfs contains user data which needs to be persistant on SW update.
Metadata (Copy 1)
Metadata (Copy 2)
#12
#13
Contains variables to manage OTA:
active_index (A or B)
previous_active_index (A or B)
Shared between TF-A and Linux
More informations in : https://developer.arm.com/documentation/den0118/a/
BOOT_PART : managed through metadata partition :
Update active_index to boot on new flashed partition
Update previous_active_index if it succeeded
BOOT_COUNT : managed in tf-a
Enable when active_index and previous_active_index are different (update ongoing)

## Slide 5: FOTA How does it work ?
Partition A is used. FOTA server requests for an update.
On available update, update manager downloads the image, and populates B partitions :
  boot_count will be enabled in tf-a in the next boot
  Performe a reboot
BL2 loads FIP partition according with active_index
When Linux (from partition B) has successfully boot, the update manager set previous_active_index
  boot_count will be disabled in tf-a in the next boot
If boot fails, BL2 increments boot_count at each reboot (ex: watchdog). When threshold is reached, BL2 selects previous active_index to boot on A partitions.
previous_active_index
active_index
0
0
previous_active_index
active_index
1
0
previous_active_index
active_index
1
1
previous_active_index
active_index
0
0